The boot menu of Clonezilla live
Here is a screenshot of Clonezilla Live boot menu:<br>
<img src="clonezilla-live/doc/02_Restore_disk_image/images/ocs-01-bootmenu.png"><br><br>

The first one is the default mode for Clonezilla Live. It will default to framebuffer mode with a resolution of 800x600.<br>
The 2nd one "(VGA 800x600 & To RAM)", is the same function with the 1st one except when Clonezilla live booting finishes, all the necessary files are copied to memory. Therefore you can remove the boot media (CD or USB flash drive) then. In addition to use the arrow key to choose, you can also press "r" to choose that.<br>
The 3rd one "(VGA with large font & To RAM)" is for you to use large font, especially when you have 4K monitor, and it will all the necessary files will be copied to memory. In addition to use the arrow key to choose, you can also press "l" to choose that.<br>
The 4th one "(Speech synthesis)" is for the blind to use, which can be chosen by pressing "s" key.<br>
There are more modes which you can choose in the 5th choice "Other modes of Clonezilla live", e.g. 1024X768 or 640x480 one if you want, as shown here:<br>
<img src="clonezilla-live/doc/02_Restore_disk_image/images/ocs-01-b-sub-boot-menu.png"><br><br>
The choice, "KMS" is for you to use <a href="http://en.wikipedia.org/wiki/Kernel_mode-setting" target=_blank>KMS (Kernel Mode Setting)</a> for your graphics card. If you have some problem to use the framebuffer mode of your graphics card, you can try it.<br>
If you do not need Chinese, Japanese or Korean environment or if your computer experiences problems in the framebuffer mode, you can choose the one "Clonezilla Live Safe graphic settings (vga=normal)" to clone in the English environment.<br>
The choice, "Clonezilla live (Failsafe mode)", is for something goes wrong when you are not be able to boot your machine, such as ACPI of your machine is not supported in the kernel.<br>

If you want to boot local OS in your hard drive, you can choose the one "Local operating system in hard drive (if available)".  This is an extra function in the boot media that has nothing to do with Clonezilla Live.<br>
The choice, "Memtester (VGA 800x600 & To RAM)" is for memory testing using <a href="https://github.com/jnavila/memtester" target=_blank>Memtester</a>. This is an extra function in the boot media that has nothing to do with Clonezilla Live.<br>
The choice, "Memory test using Memtest86+," is for memory testing using <a href="http://www.memtest.org/" target=_blank>Memtest86+</a>. This is an extra function in the boot media that has nothing to do with Clonezilla Live.<br>
The choice, "Network boot via iPXE" is used to perform a network boot via <a href="http://ipxe.org/" target=_blank>iPXE</a>. If your computer does not have a PXE network, you can use this to do boot from a network. This is an extra function in the boot media that has nothing to do with Clonezilla Live.<br>
The choice, "uEFI firmware setup" is used to enter uEFI BIOS settings.<br>